## Slide 1: Harmful Brain Activity Project Proposal
Clayton Whitteberry

## Slide 2: Project Overview
Problem: Detect six types of harmful brain activity from EEG signal and spectrogram data from critically ill patients.
The first semester will focus on data preprocessing and machine learning.
  Ensemble approach. Binary classification models used to improve accuracy of multiclass model.
The second semester will focus on deep learning.
  Vision transformer (ViT) network.

## Slide 3: Dataset
26.4 GB
Train.csv contains metadata including EEG and spectrogram ID, start times, and expert classification for the 17.3k EEGs and 11.1k spectrograms
sub EEGs are 50 second subsamples and 10k rows by 20 columns
sub spectrograms are 10 minute subsamples and 300 rows by 401 columns
Target variable has six classes: seizure, LRDA, LPD, GRDA, GPD, and other

## Slide 4: Research
Electroencephalography Signal Processing: A Comprehensive Review and Analysis of Methods and Techniques.
  Overview of Denoising Methods
Automated EEG Analysis of Epilepsy: A Review.
  Feature Extraction Overview
American Clinical Neurophysiology Society's Standardized Critical Care EEG Terminology: 2021 Version.
  Background on EEG data and the types of brain activity being detected

## Slide 5: Data Preprocessing
Dimensionality Reduction
  PCA
Noise Removal
  Internal vs. external noise
  Start with just PCA
  Add approaches like notch filtering for power line noise removal
  Another possible approach is using wavelet transform for noise removal

## Slide 6: Features
Time Domain
  Hjorth parameters (activity, mobility, complexity)
  Mean, peak to peak, skewness, etc. over smaller time intervals
  Binning to get frequency of extreme and moderate values
Frequency
  Welch function to approximate the power spectrum
  Band power: delta (0-4 Hz), theta (4-8 Hz), alpha (8-13 Hz), beta (13-30 Hz)
Time-Frequency
  Wavelet Transform
Nonlinear
  Higher order spectra, approximate entropy, and correlation dimension

## Slide 7: Modeling
First model will be a random forest
  The goal is to get initial results for comparison and also determine feature importance
Ensemble approach
  Binary classification of “other” vs. rest
  Binary classification of LRDA/LPD vs. GRDA/GPD and LRDA/GRDA vs. LPD/GPD
  Random Forest multiclass classification

## Slide 8: Progress
Checked target class balance
  Slightly imbalanced with seizure data accounting for 20% of the dataset and LPD data accounting for 14% of the dataset
Removed EEGs and spectrograms with more than 20% missing data
  5k of 107k rows removed from dataset
  Didn’t significantly impact the balance of the target variable
Split dataset by target class to get six dataframes