## Slide 1: Harmful Brain Activity Classification
Clayton Whitteberry

## Slide 2: Overview
Multiclass Target (Brain Activity)
  Seizure
  Lateralized Periodic Discharge
  Generalized Periodic Discharge
  Lateralized Rhythmic Delta
  Generalized Rhythmic Delta
  Other
106.8k sub EEGs and sub spectrograms
  Sub EEG Dimensions
    10k rows by 20 columns
  Sub Spectrogram Dimensions
    300 rows by 401 columns

## Slide 3: EEG Background
Key Advantage
  Non-invasive measure of brain activity that is measured at the speed the brain activity is happening
Key Disadvantage
  Electrodes highly sensitive
    Pick up broad range of signals inside and outside the brain
    Resulting EEG signals can have high amounts of noise

## Slide 4: Objective: EEG Preprocessing
Denoising
Principal Component Analysis (PCA)
Independent Component Analysis (ICA)
Frequency Filtering
Dimensionality Reduction
Principal Component Analysis (PCA)
Grouping and Averaging Signals

## Slide 5: PCA Only (Left/Right Electrodes)
Principal Component Analysis (PCA)
Grouped scalp electrodes by left and right hemisphere
  11 in each group
Reduced to 3 components
  > 80% variance explained
PCA alone not sufficient to handle denoising
  Power line noise (spikes at 60 Hz) still present

## Slide 6: ICA-PCA
Independent Component Analysis (ICA)
ICA prior to PCA hurts PCA results
8 components required to explain more than 70% of variance

## Slide 7: Averaging Signals for ICA
Grouped scalp electrodes according to spectrogram groupings
  Right/Left Parasagittal
  Right/Left Lateral
  Central
Averaged Signals within Groups
  Reduces 19 columns to 5
Advantages
  Dimensions reduced before ICA
  Approach similar to spectrogram generation

## Slide 8: Filtering EEG Signals with MNE
Filters Applied
  Low Frequency (1 Hz)
  High Frequency (70 Hz)
  Notch Filter (60 Hz)

## Slide 9: Effects of Filter on Power Spectrum
Notch filter seen clearest
  Spike at 60 Hz removed

## Slide 10: Capstone II
Finish EEG preprocessing
Evaluate/Improve Filtering Results
ICA artifact repair/removal
Feature Extraction
Time-Frequency Analysis
Non-Linear Analysis
Modeling
Ensemble approach

## Slide 11: ICA Artifact Detection
Example
  Blink Artifact Detection

## Slide 12: Feature Extraction
Time-Frequency
Short-time Fourier Transform
Wavelet Transform
Frequency Band Power
Nonlinear
Higher Order Spectra
Approximate Entropy
Noise Immunity
Measure of Regularity

## Slide 13: Modeling
Common Models
Random Forest
Alternative
XGBoost
Used for seizure specific tasks
SVM